# Van’s Aircraft RV-6A

# Pilot’s Operating Handbook

N686MS

PERFORMANCE – SPECIFICATIONS

SPAN: ………………………………………………………………..	23’ 0”

LENGTH: …………………………………………………………….	19’ 9”

HEIGHT:  …………………………………………………………….	6’ 8”

SPEED:

Maximum at Sea Level ……………………………………..	182 Knots

Cruise, 75% Power at 8,000 Ft ……………………………..	167 Knots

RANGE (includes 3 gal. for taxi, takeoff & climb):

75% @ 8000’ , no reserve .………………………………….	695 nm

55% @ 8000’  no reserve ….……………………………….	840 nm

75% @ 8000’, one hour (8 gal) reserve ……………………..	540 nm

55% @ 8000’, one hour (8 gal) reserve ……………………..	650 nm

RATE OF CLIMB AT SEA LEVEL …………………………….….	2,050 FPM

SERVICE CEILING …………………………………………..…….	19,500 FT

TAKEOFF PERFORMANCE: ……………. ……………….………	535 Ft

LANDING PERFORMANCE: ………………..…………….………	500 Ft

STALL SPEED (CAS):

Flaps Up, Power Off ………………………………………	47 Knots

Flaps Down, Power Off ……………………………………	43 Knots

MAXIMUM WEIGHT (Normal Category): ………………………….	2000 Lbs

EMPTY WEIGHT ………………………………………….		1189 Lbs

MAXIMUM USEFUL LOAD: ……………………………………..	811 Lbs

BAGGAGE ALLOWANCE …………………………………………	 83 Lbs

WING LOADING (Pounds/ Sq. Ft) …………………………………	17.27

POWER LOADING (Pounds/ HP) ………………………………….	10.5

FUEL:

Capacity ……………………………………………		38 Gal Total

Type ……………………………………………………….	100 LL

OIL CAPACITY …………………………………………………….	8 Qts

ENGINE: Lycoming ………………………………………………..	O-360-A1A

PROPELLER: Hartzell …………………………………….   	HC-C2YL-1BF

AIRSPEED LIMITATIONS

|  | SPEED | KIAS | REMARKS |
| --- | --- | --- | --- |
| VNE | Never Exceed Speed | 182 Kts | Do not exceed this speed in any operations. |
| VNO | Maximum Structural Cruising Speed | 156 Kts | Exceed this speed only in smooth air. |
| VA | Maneuvering Speed | 115 Kts | Do not make full control movements above this speed. Full elevator deflection will result in a 6g load at this speed. |
| VFE | Maximum Flap Extended Speed | 96 –20 deg 87 - Full | Do not exceed this speed with flaps down |
| Vy | Best Rate of Climb | 75 Kts |  |
| Vx | Best Angle of Climb | 65 Kts |  |
| Vs | Stall Speed Clean | 47 Kts |  |
| Vso | Stall Speed Landing Configuration | 43 Kts |  |

AIRSPEED INDICATOR MARKINGS

| MARKING | KIAS VALUE OR RANGE | SIGNIFICANCE |
| --- | --- | --- |
| White Arc | 43 – 87 Kts | Full Flap Operating Range. Lower limit is Vso. Upper limit is maximum speed with flaps extended |
| Green Arc | 47 – 156 Kts | Normal Operating Range. Lower limit is Vs. Upper limit is maximum structural cruising speed |
| Yellow Arc | 156 – 182 Kts | Operations must be conducted with caution and only in smooth air. |
| Red Line | 182 Kts | Maximum speed for all operations |

## Views

##### AEROBATIC INFORMATION

Weight Limitation – 1375 Pounds

Recommended Entry Speeds:

Loops, Horizontal Eights 	120 – 165 Kts

Immelman Turns 		130 – 165 Kts

Aileron Rolls, Barrel Rolls 	105 – 165 Kts

Snap Rolls			70  –   95 Kts

Vertical Rolls 			155 –165 Kts

Split-S 				85  -  95 Kts

##### PREFLIGHT INSPECTION

1.	CABIN

- Documentation -- Available In Airplane

- Aeronautical Charts – CURRENT AND APPROPRIATE TO FLIGHT

- Seat Belt Securing Control Stick --  RELEASE

- Ignition Switch  -- OFF

- Avionics -- OFF

- Master Switch -- ON

- Engine Monitor – ON

- Engine Monitor –  RESET FLIGHT TIME

- Fuel Quantity -- CHECK QUANTITY
			      -- VERIFY ENGINE MONITOR PRESET

- Flaps – DOWN

- Master Switch -- OFF

- Carb Heat – COLD

2. EMPENNAGE

- Tail Tie-Down -- DISCONNECT

- Control Surfaces -- CHECK freedom of movement and security

- Static Sources (both sides of fuselage) –CHECK for blockage

3. RIGHT WING

- Aileron -- CHECK freedom of movement and security

- Flap -- CHECK security

- Wing Tie-Down -- DISCONNECT

- Main Wheel Tire -- CHECK for proper inflation

- Chock -- REMOVE

- Right Wing Tank – SUMP

- Fuel Quantity -- CHECK VISUALLY

Fuel Filler Cap – SECURE

5. NOSE

- Engine Oil Level -- CHECK, do not operate with less than 4 quarts

- Propeller and Spinner -- CHECK for nicks and security

- Cowl Hinge Pins – CHECK for security

- Air Inlet -- CHECK for restrictions

- Nose Wheel Tire -- CHECK for proper inflation

- Master sw – ON

- Fuel Boost Pump – ON

- Gascolator – SUMP

- Fuel Boost Pump – OFF

- Master sw -- OFF

- Chock -- REMOVE

- Fuel Tank Vents -- CHECK for blockage

6. LEFT WING

- Wing Tie-Down -- DISCONNECT

- Main Wheel Tire -- CHECK for proper inflation

- Chock -- REMOVE

- Left Wing Tank -- SUMP

- Fuel Quantity -- CHECK VISUALLY

- Fuel Filler Cap -- SECURE

- Pitot Tube Cover -- REMOVE and check for blockage

- Landing Light -- CHECK condition

- Aileron -- CHECK freedom of movement and security

- Flap -- CHECK security

#### BEFORE STARTING ENGINE

- Preflight Inspection -- COMPLETE

- Seat Belts and Shoulder Harnesses -- ADJUST and LOCK

- Fuel Selector Valve -- DESIRED TANK

- Avionics and Electrical -- OFF

- Brakes -- SET

- Circuit Breakers -- CHECK IN

- Canopy adjust

#### STARTING ENGINE (cold)

- Mixture -- LEAN

- Throttle to 1/8

- Prop -- HIGH RPM

- Master Switch – ON

- Flaps -- UP

- Fuel Boost Pump -- ON

- Prime – Mix to rich (4-5 seconds when cold)

- Fuel Boost Pump -- OFF

- Propeller Area -- CLEAR

- Ignition Switch -- START

- Alt. Field, Avionics & Instruments – ON

- Oil Pressure -- CHECK   25  psi at idle

- Position & Strobe – ON

### STARTING ENGINE (Warm)

- Mixture -- LEAN

- Throttle to 1/8

- Prop -- HIGH RPM

- Master Switch – ON

- Flaps -- UP

- Fuel Purge Lever -- Pull

- Fuel Boost Pump – ON (5-10 seconds to purge)

- Fuel Boost Pump -- OFF

- Propeller Area -- CLEAR

- Ignition Switch -- START

- Alt. Field, Avionics & Instruments -- ON

- Oil Pressure -- CHECK   25  psi at idle

- Position & Strobe – ON

BEFORE TAKEOFF

- Brakes -- SET

- Canopy  -------- Main Latch – SECURE

- Flight Controls -- FREE and CORRECT

- Flight Instruments – SET
        	Altimeter – CORRECT PRESSURE
         	D/G – CORRECT HEADING
    		A/H – ALLIGNED 
        	G-Meter – RESET

GPS ON

- Fuel Selector Valve -- DESIRED TANK

- Mixture -- RICH (below 3000’)

- Elevator and Aileron Trim -- NEUTRAL

- Throttle -- 1700 RPM

- Magnetos --  CHECK (125 max drop, 50 differential)

- Suction – CHECK  (5” Hg)

- Prop – cycle CHECK operation

- Engine Instruments -- CHECK

- Throttle -- IDLE

- Radios -- SET

- Fuel Boost Pump -- ON

- Transponder – ALTITUDE

- Passenger – READY and willing

##### TAKEOFF

#### NORMAL TAKEOFF

- Wing Flaps – UP

- Prop – HIGH RPM

- Throttle --  FULL OPEN

- Elevator Control – LIFT NOSE WHEEL (at 55KIAS)

- Climb Speed --  110 KIAS

#### SHORT FIELD TAKEOFF

- Wing Flaps – 10 Deg

- Prop – HIGH RPM

- Brakes – APPLY

- Throttle – FULL OPEN

- Mixture – RICH (above 3000’ lean to obtain max RPM)

- Brakes – RELEASE

- Climb Speed – 80 KIAS (Vy)

##### ENROUTE CLIMB

- Airspeed – 110 - 130 KIAS

- Throttle – 25 in Hg, or full throttle

- Prop – 2500 RPM

- Boost Pump – OFF at 1000 feet AGL

- Fuel Pressure – CHECK

- Mixture – LEAN above 5000’

##### CRUISE

- Throttle – 23 in Hg

- Prop – 2300 RPM

- Trim – ADJUST

Mixture – LEAN to 50 deg C rich of peak

##### POSTFLIGHT

##### AFTER LANDING

- Wing Flaps – UP

- Boost Pump – OFF

- Transponder – STANDBY

ENGINE SHUTDOWN

- Flaps – DOWN

- Prop – FULL FORWARD

- Throttle – IDLE

- CHT decidedly dropped

- All electrical sw  – OFF

- Avionics and Instr.-- OFF

- Mixture – IDLE CUT-OFF

- Wait for shut down

- Master – OFF

#### SECURING AIRCRAFT

- Wheel Chocks

- Wing & Tail Tie-Down

- Pitot Tube Cover

- Cockpit

- Ignition Key – REMOVED

- Master and Electrical Switches – OFF

##### Performance

Cruise Performance at 8,000’:

| KTAS | RPM | MAP | Fuel Flow | % Power |
| --- | --- | --- | --- | --- |
| 167 | 2400 | 23” | 8.4 GPH | 75% |
| 157 | 2200 | 23” | 7.4 GPH | 65% |
| 151 | 2200 | 21” | 6.3 GPH | 55% |

No Wind Range at 8,000’:

- All range calculations include 3 gal. for engine start, taxi, takeoff and climb.

- Engine is leaned for best economy.

One hour (8 gal.) reserve:

75% Power ………………………………………………..	540 nm

65% Power ………………………………………………..	575 nm

55% Power ………………………………………………..	650 nm

No Reserve:

75% Power ………………………………………………..	695 nm

65% Power ………………………………………………..	745 nm

55% Power ………………………………………………..	840 nm

##### WEIGHT AND BALANCE DATA

Make: Michael Stewart			Model:  RV-6A

Serial: 25708				Registration: N686MS

Maximum Weights:

Aerobatic Category …………………………	1375 Lbs

Utility Category …………………………….	1650 Lbs

Normal Category ……………………………	2000 Lbs

Datum= 60 inches forward of wing leading edge (L.E.)

Design C.G. Range = 	15% to 29% of wing chord

8.7” to 16.8” from L.E.

68.7” to 77.1” aft of Datum

Wing L.E. = 60 inches aft of datum

Main wheel right = 84.25” aft of datum

Main wheel left =   84.25” aft of datum

Nose wheel =          28.50” aft of datum

Fuel ……………………	70” aft of datum

Pilot and Passenger ……	87.4” aft of datum

Baggage ……………….	117” aft of datum

Aircraft weighed empty in level flight attitude.

(Includes 8 qts. of oil, no fuel)

Sample:

Weight		Arm		Moment

Aircraft		1189				83504

Fuel (6lbs/gal)			70

Pilot				87.4

Passenger			87.4

Baggage			117

Total

CG = Total Moment / Total Weight

CG = 		 in aft of datum

CG Range = 68.7 to 77.1 in aft of datum

Empty CG = 70.23

##### WEIGHT AND BALANCE DATA

*All CG ranges for possible flight conditions are within design limits

|  | Left Main | Rt. Main | Nose |  | Total |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| weight | 447 | 443 | 299 |  | 1189 |  |  |  |
| Component | Weight | * | Arm | = | Moment |  |  |  |
| Lmain | 447 |  | 84.25 |  | 37659.75 |  |  |  |
| Rmain | 443 |  | 84.25 |  | 37322.75 |  |  |  |
| Nose | 299 |  | 28.5 |  | 8521.5 |  |  |  |
| sub total |  |  |  |  |  | 83504 |  |  |
| CG Range | 68.7 to 77.1 in aft of datum |  |  |  |  |  |
| Empty C.G | 70.23 |  |  |  |  |  |  |  |
| Max. Gross Weight |  |  |  | Full Baggage, No Pax |  |
| Item | Weight | Arm | Moment |  | Item | Weight | Arm | Moment |
| Aircraft | 1,189 |  | 83,504 |  | Aircraft | 1,189 |  | 83,504 |
| Fuel (6 lbs/gal) | 228 | 70 | 15,960 |  | Fuel (6 lbs/gal) | 228 | 70 | 15,960 |
| Pilot | 250 | 87 | 21,750 |  | Pilot | 250 | 87 | 21,750 |
| Passenger | 250 | 87 | 21,750 |  | Passenger | 0 | 87 | 0 |
| Baggage | 83 | 117 | 9,711 |  | Baggage | 83 | 117 | 9,711 |
| Total | 2,000 |  | 152,675 |  | Total | 1,750 |  | 130,925 |
| CG: | 76.3375 |  |  |  | CG: | 74.81 |  |  |
| Zero Fuel CG | 77.15 |  |  |  | Zero Fuel CG | 75.54 |  |  |
| Pilot, Pax, No Baggage |  |  |  | Pilot, No Pax, No Baggage |  |  |
| Item | Weight | Arm | Moment |  | Item | Weight | Arm | Moment |
| Aircraft | 1,189 |  | 83,504 |  | Aircraft | 1,189 |  | 83,504 |
| Fuel (6 lbs/gal) | 228 | 70 | 15,960 |  | Fuel (6 lbs/gal) | 228 | 70 | 15,960 |
| Pilot | 250 | 87 | 21,750 |  | Pilot | 200 | 87 | 17,400 |
| Passenger | 250 | 87 | 21,750 |  | Passenger | 0 | 87 | 0 |
| Baggage | 5 | 117 | 585 |  | Baggage | 5 | 117 | 585 |
| Total | 1,922 |  | 143,549 |  | Total | 1,622 |  | 117,449 |
| CG: | 74.69 |  |  |  | CG: | 72.41 |  |  |
| Zero Fuel CG | 75.32 |  |  |  | Zero Fuel CG | 72.804 |  |  |

##### Engine Information

Model: ……..	Lycoming O-360 A1A, Fuel Injected

HP: …………	180

Fuel: ………..	91/96 or 100/130 octane minimum

………..	100LL

Oil Filter: …..	Champion CH48110

OIL:  Avg	MIL-L-6082	Ashless Dispersant

Ambiant Air	   Grades		     Grades

Above 80F	SAE 60		      SAE 60,20w50

Above 60F	SAE 60		      SAE 60

30 – 90F		SAE 40		      SAE 40,50

0-70F		SAE 30		      SAE 30,40 or SAE 40

###### Below 10F		SAE 20		      SAE 30 or 20w30

###### Oil Sump Capacity …….. 8 U.S. Quarts

###### Minimum Safe Quantity ...2 U.S. Quarts

###### Operating Conditions:

###### Oil Inlet Temp:		82 deg C desired, 118 deg C Maximum

###### Oil Pressure:		95 psi max; 	 55 psi min; 	 25 psi idle

###### Fuel Pressure:		 ? psi max;	 ? psi min;	 ? psi desired

###### Cyl. Head Temp	66 deg C – 205 deg C desired range,  260 deg C max

###### Max oil consumption .45qts/hr. at cruise

###### Conversion table:

| Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 | 50 | 60 | 140 | 110 | 230 | 160 | 320 | 210 | 410 |
| 16 | 60 | 66 | 150 | 116 | 240 | 166 | 330 | 216 | 420 |
| 21 | 70 | 71 | 160 | 121 | 250 | 171 | 340 | 221 | 430 |
| 27 | 80 | 77 | 170 | 127 | 260 | 177 | 350 | 227 | 440 |
| 32 | 90 | 82 | 180 | 132 | 270 | 182 | 360 | 232 | 450 |
| 38 | 100 | 88 | 190 | 138 | 280 | 188 | 370 | 238 | 460 |
| 43 | 110 | 93 | 200 | 143 | 290 | 193 | 380 | 243 | 470 |
| 49 | 120 | 99 | 210 | 149 | 300 | 199 | 390 | 249 | 480 |
| 54 | 130 | 104 | 220 | 154 | 310 | 204 | 400 | 254 | 490 |

EMERGENCY PROCEDURES

AIRSPEEDS FOR EMERGENCY OPERATIONS

Engine Failure After Takeoff:

Wing Flaps Up …………………………	80 Kts

Wing Flaps Down ……………………..	70 Kts

Maneuvering Speed (Va) ……………………….	115 Kts

Maximum Glide ………………………………… 	80 Kts

ELECTRICAL / ALTERNATOR FAILURE

- Avionics –OFF

- Master Switch – OFF, both sides

- Master Switch – ON

IF ALTERNATOR IS STILL OFF-LINE:

- Master Switch – OFF

- Electrical Switches – OFF

- Alternator Breaker – PULL

- Avionics – OFF

- Main Feed Breaker – PULL

- Alternate Feed Switch Guard – UP

- Alternate Feed Switch – ON

- Avionics – ON as required

- Electrical Equipment – ON, as required

- Flight – TERMINATE as soon as practical,  aircraft is on battery reserves only.

EMERGENCY PROCEDURES

ENGINE FAILURES

ENGINE FAILURE DURING TAKEOFF RUN

- Throttle –IDLE

- Brakes – APPLY

- Wing Flaps – RETRACT

- Mixture – IDLE CUT-OFF

- Ignition Switch – OFF

- Master Switch – OFF

ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF

- Airspeed – 70 KIAS

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Ignition Switch – OFF

- Wing Flaps – AS REQUIRED

- Master Switch – OFF

ENGINE FAILURE DURING FLIGHT

- Airspeed –80 Knots

- Boost Pump – ON

- Fuel Selector – SWITCH TANKS

- Mixture – RICH

- Ignition Switch – BOTH, LEFT, RIGHT

- Transponder – 7700

EMERGENCY PROCEDURES

FIRES

DURING START ON GROUND

- Cranking – CONTINUE, to get a start which would suck the flames and accumulated fuel through the carb and into the engine.

If engine starts:

- Power – 1700 RPM for a few minutes

- Engine – SHUTDOWN and inspect for damage

If engine fails to start:

- Throttle – FULL OPEN

- Mixture – IDLE CUT-OFF

- Cranking – CONTINUE

- Fire Extinguisher – OBTAIN

- Engine – SECURE

ENGINE FIRE IN FLIGHT

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Master Switch – OFF

- Cabin Heat and Air – OFF

ELECTRICAL FIRE IN FLIGHT

- Master Switch – OFF

- Avionics – OFF

- All Other Switches (except ignition) – OFF

- Vents/ Cabin Air/ Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

CABIN FIRE

- Master Switch – OFF

- Vents/ Cabin Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

WING FIRE

- Nav & Strobe Lights – OFF

- Landing Light – OFF

FAR 91.125 - ATC light signals.

ATC light signals have the meaning shown in the following table:

| Color and type of signal | Meaning with respect to aircraft on the surface | Meaning with respect to aircraft in flight |
| --- | --- | --- |
| Steady green | Cleared for takeoff | Cleared to land |
| Flashing green | Cleared to taxi | Return for landing |
| Steady red | Stop | Give way to other aircraft and continue circling. |
| Flashing red | Taxi clear of runway in use | Airport unsafe—do not use |
| Flashing white | Return to starting point on airport | N/A |
| Alternating red and green | Exercise extreme caution | Exercise extreme caution |

## Compass Headings, VFR under 18,000ft

| Course | Altitude |
| --- | --- |
| 0 – 179 degrees | Odd thousand +500 |
| 180 – 360 degrees | Even thousand + 500 |